Part I
Organic analysis, thermodynamic and general mechanics

---
General
Definition
The internal combustion engine is a machine which transforms the chemical energy contained in a fuel into heat energy released by the combustion of the fuel and then into mechanical motive energy. This transformation is carried out during an engine cycle which represents a complex physico-chemical process repeating periodically in the engine cylinder over 4 operations: Intake, compression, ignition-expansion and exhaust.

---
Terminology (Fig. 1)
Bore (D)
Raceb (C)
Cylinder (V)
Fig. 1

---
2. Comparison between the operation of gasoline and diesel engines
Cycle	Diesel	Gasoline
1 st stoke, Admission	Air alone	Air + gasoline mixture
2 nd stoke, Compression	- compression ratio 30 to 40 bars / - Temperature rise 500 to 600 C	compression ratio 10 to 12 bars / Temperature rise 320 to380 C
3 th stoke, Engine time	Combustion relaxation injection of sprayed diesel / Self-ignition gas expansion Gas / Temperature 1800 °C	- Explosion controled by an electrical spark / -Gas temperature of 2000 °C
4 rd stoke, Exhaust	-Hiighly toxic gas	Low toxic gas
Specific consumption	- 215 to 300 g/kW/h	301 to 405 g/kW/h

---
2. The characteristic performances of an MCI
- Are the parameters indicated and the effective parametersThe parameters indicated characterize the actual cycle considered. They only take into account heat losses from the real cycle
These losses are due to: - The transmission of heat through the walls. - Incomplete combustion even in rich areas - Motor fluid leaks - The dissociation of CO2 molecules at high temperature by absorbing heat
To pass from the indicated parameters to the actual parameters of the motor, it is necessary to take into account the part of the mechanical losses
- So, the term performance refers to the characteristics of the engine; efficiency, power, work... they allow us to compare two different engines.

---
indicated
Mechanical loss
Parameters indicated
Thermal loss
Useful energy on the motor shaft
Combustion energy
Effective (parameters)settings

---
- Effective average pressure Pme: is the ratio of the work provided by the engine during a cycle We and the displacement of the engine V0
- Effective or real power
- Average pressure indicated Pmi is a pressure assumed to be constant during the trigger stroke which would give the same area
- Indicated power

---
3.1. Parameters related to engine performance
- Specific fuel consumption (Cs): is the ratio between the hourly mass consumption (g/h) and the real power
in g/Wh
- Calorific value of fuel (Pc): is the ratio between the energy of combustion and the mass of the fuel
in J/g

---
theoretical yield
Yield indicated
Internal performance
Mechanical performance
Overall performance

---
4. Chemical analysis
internal combustion engine releases large quantities of carbon dioxide, water vapor, nitrogen oxides, CO, HC and low-level soot into the air through the exhaust
To determine the nature and chemical composition of an ICE's emissions into the atmosphere, organic analysis is carried out
4.1. Definition
Organic analysis groups together the various chemical methods that aim to identify the composition and chemical structure of substances. It can be elementary or functional..

---
Elemental analysis characterizes the chemical element composition of organic molecules. It can be:qualitative: aims to identify the main components of a substance (Fig. 3).
Fig. 3

---
quantitative: determines the quantity of the main atoms in the molecules of a substance in order to know their chemical structure (Fig. 4).
Fig. 4

---
Quantitative elemental analysis is divided into:
Chemical methods:
acid attack followed by combustion analysis with an elemental analyzer
Schöniger oxidation: determination of halogens, sulfur and phosphorus;
Kjeldahl method: determination of nitrogen;
Physical methods:
     atomic spectrometry.

---
Example
The combustion of 1.14 g of a fuel CxHy gives 3.52 g of CO2 and 1.62 g of water vapor, the density of CxHy relative to air is d=3.91
Write the combustion equation.
Determine the chemical composition of the fuel.
Solution
2CxHy + (2x+y/2) O2 =>2 xCO2 + yH2O
M= 29d=114 g=24x+2y
The chemical composition of fuel C8H18