Part II
 Main cinematic chain and functional auxiliaries

---
Part II - Main cinematic chain and functional auxiliaries
1- kinematic chain
All the components (Fig. 1) of the vehicle allowing its movement are called “kinematic chain” and are made up of:
- Engine
- The clutch
- Gearbox
- Drive shaft
- Wheels
Fig. 1

---
1.1- The engine
The role of the engine is to transform the heat energy of the fuel into mechanical energy. It causes the fuel to burn to create the energy that will be used to move the wheels. The rest of the driveline transports and transforms this energy to the wheels.
1.2. The clutch
The clutch couples or uncouples the engine with the rest of the chain to allow shifting (Fig. 2).
Fig. 2

---
2.3. The gearbox
The gearbox transforms the engine torque to adapt it to the resistance force created by the movement of the vehicle. The interest of the gearbox is twofold. First of all, it makes it possible to compensate for the lack of flexibility of the internal combustion engine which can only vary within
fairly narrow speed limits. In addition, it ensures that the engine is always in optimal operating mode. Changing speed, by increasing or on the contrary reducing the number of engine revolutions, ensures that despite the variation in vehicle speed, the engine rotation speed is always the same (Fig. 3).
Fig. 3

---
2.4. The transmission shaft
The transmission shaft transmits the movement of the gearbox to the axle (Fig. 4). It exists: - Longitudinal drive shafts arranged between the gearbox and the axle (rear-wheel drive vehicle) - Wheel shafts or motor half-shafts arranged between the axle and the drive wheels.
Fig. 4

---
2.5. The bridges
 There are motor bridges (which transmit the movement) and directional bridges (which act on the direction). The directional bridges are connected to the steering controls and allow the vehicle to be steered while moving. All of the bridges also provide a reduction in speed (single or double), which allows an increase in the power of the movement. In addition, they include a differential that allows the wheels to turn at different speeds and therefore the vehicle to turn without skidding (in a turn, the wheels on the outside travel more distance).

---
2. Functional Auxiliaries
No modern internal combustion engine is capable of operating independently. This is because the fuel must be delivered from the gas tank to the engine
The rotating parts require constant lubrication. Due to the high temperatures generated by combustion, the engine must be cooled. These accompanying processes are not provided by the engine itself, so the internal combustion engine operates with auxiliary systems.

---
The auxiliary chain of the internal combustion engine is composed of the following systems:
Ignition system
Fuel system
Cooling system
Lubrication system
Distribution system
Exhaust system

---
2.1. Fuel system
Battery ignition is still used, but is increasingly being replaced by the more efficient and reliable electronic ignition (Fig. 5).
Fig. 5

---
Gasoline Engine
In gasoline engines, the most commonly used carburetor currently. The gasoline enters through the intake valves connected to the camshaft.
Diesel Engine
The diesel engine relies on the injection system. It puts the fuel under pressure and injects it. The fuel is thus ejected into the air that has been compressed to high pressure in the combustion chamber

---
2.3. Cooling system
Is the set of mechanisms that serve to evacuate heat energy not transformed into mechanical energy. Most often, it is water with an additive to increase the boiling temperature and frost resistance (Fig. 6).
This system is composed of:
• Water jackets
• Radiator
• Fan
• Water pump
• Thermostat
Fig. 6

---
2.4. Lubrication system
Continuous lubrication affects all moving mechanisms, it consists of a system of pipes which, via a pump, brings the lubricant to the various parts (bearings, bushings, ball bearings) to be lubricated (Fig. 6).
Fig. 6

---
The main components of this system are:
• The oil filter:
It retains impurities suspended in the oil that originate from
Combustion residue particles.
Particles from wear of parts.
deterioration of the oil
• The oil pump:
It sucks the oil from the lower crankcase and directs it under pressure, through the pipes, to the elements to be lubricated
 • The oil sump:
It serves as a reserve of lubricating oil and also contributes to its cooling

---
2.5. Distribution system
The circular movement of the crankshaft is transmitted to the camshaft through a system called "distribution system"
since it is responsible forusing and distributing
the force transmitted by the bottom of the engine
 to the entire engine and thus Making the Elements
work together (Fig. 7)
.The distribution is done by:
Metal
Cascade of pinions
Belt
Fig. 7

---
2.6. Exhaust system (Fig. 8)
Fig. 8

---
2.6. Exhaust System
The exhaust system refers to the circuit that redirects combustion gases from the engine, usually located at the front of the vehicle, to the outside environment.
The main components of the exhaust system are:
Exhaust manifold
Catalytic converter
Oxygen sensor
Muffler
Helmholtz tuning chambers

---
The exhaust manifold :
 receives the exhaust gases from the engine. The manifold reduces the noise level of combustion and transports heat to the rear of the vehicle to enhance the oxidation of unburned hydrocarbons and carbon monoxide.
The oxygen sensor :
optimizes the efficiency and performance of the vehicle by taking into account all variable parameters: engine speed, engine temperature, air temperature, coolant temperature, and more.

---
The muffler :
 reduces exhaust noise by directing it into compartments known as Helmholtz resonator chambers.
The catalytic converter :
is located much further along in the exhaust system. This component is specifically designed to convert toxic exhaust gases into carbon dioxide, which is non-aggressive, and water vapor through a chemical reaction that requires catalysts.