## Slide 1
Part III
Respirations: operational modes, aspiration, and SUPERCHARGING

## Slide 2
Part III - Respirations : operational modes, aspiration and supercharging
Intake in an Internal Combustion Engine
The first phase of the cycle is the intake (admission): the intake valve is open (the exhaust valve remains closed) and the piston moves down.
1.1. Intake in a Gasoline Engine
The air-fuel mixture is drawn into the combustion chamber.
1.2. Intake in a Diesel Engine
The first phase is the intake: the cylinder draws in clean air through the intake valve, and as the air is compressed, diesel is injected at the end of the intake phase.
.

## Slide 3
The internal combustion engine does not have very good efficiency with the classic intake mode (via piston movement). Several solutions have been proposed to increase the specific power of this engine:
Increasing the engine's rotational speed is a solution used in competition; however, this technique leads to multiple wear issues within the engine and reduces its lifespan. The engine's fuel consumption and pollution also increase when using this technique. All these disadvantages reduce reliability and make it unable to meet current automotive engine construction standards.
Part III - Respirations : operational modes, aspiration and supercharging

## Slide 4
A simpler solution is to increase the engine displacement by either increasing the unit displacement or the number of cylinders. The increase in mass, engine size, and consumption are drawbacks that penalize this technique.
Another approach is to send more air into the engine. Instead of limiting it to the engine's natural intake, a system is added that will also "blow" a lot of air inside. This technique is called supercharging.
Part III - Respirations : operational modes, aspiration and supercharging

## Slide 5
Part III - Respirations : operational modes, aspiration et supercharging
2. Supercharging an Engine
Supercharging is a process aimed at increasing the efficiency of an internal combustion engine without increasing its rotational speed. This technique allows for more air to be sent into the engine. Instead of being limited to the engine's natural intake, a system is added that also "blows" a significant amount of air inside. This way, it is also possible to increase the amount of fuel and thus the combustion. A turbocharger works well at high RPMs because it is powered by exhaust flows, which are greater at high speeds.

## Slide 6
"Supercharging allows:
Improving cylinder filling
Reducing pollution
Increasing engine torque
Supercharging is based on the use of a compressor or an exhaust turbocharger. For example, the specific power of engines increases from ~55 hp/l to values exceeding 100 hp/l thanks to various solutions improving the filling."
Let me know if you'd like any further assistance!
Part III - Respirations : operational modes, aspiration and supercharging

## Slide 7
3. The different types of supercharging 3.1. The turbocharger
The turbocharger, more commonly known as a "turbo," is the most widely used supercharging system in the automotive sector.
The turbo operates like a centrifugal pump. Due to the effect of centrifugal force, caused by a
high rotational speed (~150,000 rpm)
, the intake air is pushed towards the
periphery of the compressor wheel,
resulting in suction at its center (Fig. 1)."
Fig. 1
Part III - Respirations : operational modes, aspiration and supercharging

## Slide 8
- Once this turbine is in action, it will compress the air, which will then be directed to the combustion chambers. With the air-fuel mixture being more oxygenated, the explosions generated by the pistons will be stronger, giving the engine more power
The exhaust gas flow drives turbine '1' (Fig. 2). The movement is directly transmitted to compressor '2' via a connecting shaft. The compressor supplies the engine with pressurized air.
Fig. 2
Part III - Respirations : operational modes, aspiration and supercharging

## Slide 9
Fig. a-3
Fig. b-3
Exhaust gas circulation and the gas compressed by the turbocharger (Fig. a and b 3)."
Part III - Respirations : operational modes, aspiration and supercharging

## Slide 10
The more the engine filling increases, the more effective the turbo becomes. The more effective the turbo is, the more the filling increases... (Fig. 4).
Part III - Respirations : operational modes, aspiration and supercharging
Fig. 4

## Slide 11
When the desired pressure is reached, a bypass '1' controlled by a valve '2' reduces the exhaust gas flow driving the turbo’s turbine, thus limiting its rotational speed (Fig. 5).
Fig. 5
Part III - Respirations : operational modes, aspiration and supercharging

## Slide 12
Part III - Respirations : operational modes, aspiration and supercharging
an intercooler enhances the performance of the supercharging system (Fig. 6). Every 10°C decrease in intake temperature allows for a power increase of ~3%.
Fig. 6
4. Cooled supercharging
The increase in intake pressure leads to a significant rise in the temperature of the mixture (20°C at the turbo inlet, >100°C at the outlet). The improvement in filling is not as significant as it could be. Cooling the air (intake temperature ~50°C) using